## Slide 1
Mass
Transfer
GROUP 13
Mayur Dilip Pachpute | 240643
Priyanshu | 240805
Ravi Kasotiya | 240855
Roushan Upadhyay | 240886
CHE-213

## Slide 2
Problem: Limitations of Manual Observation
  Fatigue & Human Error: Counting tiny drops (2–4 mm) by eye over long extraction periods inevitably leads to eye strain, missed counts, and corrupted data.
The Core Concept: A Software-Driven Observer
  The AS-DMTS Framework: Upgrading the laboratory setup by replacing manual human observation with a relentless, high-speed "Digital Eye" using OpenCV.
  Beyond Simple Counting: The software doesn't just tally drops; it maps the entire column and extracts spatial data (pixel coordinates, bounding boxes) that a human could never measure on the fly.

## Slide 3
  Digital Pre-Processing: We use tools like Contrast Enhancement (CLAHE) and Background Subtraction to digitally strip away laboratory distractions, allowing the algorithm to "see" better than a human.
The Hypothesis
  If we digitize the observation process using a background-subtracted tracking matrix, we can completely eliminate human error..
  Expected Outcome: This digital framework will yield 100% counting accuracy, remove subjective bias, and operate continuously without fatigue.

## Slide 4
2
  ROI Isolation: Cropped the frame horizontally to isolate the fluid column, discarding dead space to optimize processing speed (FPS).
  Contrast Enhancement (CLAHE): Applied Contrast Limited Adaptive Histogram Equalization. Because the fluid is bright, CLAHE artificially darkens the faint edges of the droplets to make them machine-readable.
  Gaussian Blurring: Implemented a 7 X 7 blur matrix to merge the top and bottom edges of the "hollow" looking bubbles into solid, detectable masses.
  MOG2 Background Subtraction: Extracted moving blobs by isolating pixel variations over a 500-frame history while ignoring static background lighting.
Methodology

## Slide 5
3
  Bounding Box Extraction: Applied cv2.boundingRect() to draw coordinates (x, y, w, h) around moving contours.
  Aspect Ratio Calculation: To prevent the code from counting tall, thin vertical glare stripes as drops, we calculate the aspect ratio:
AR = w/max(1, h)
  Only blobs with an AR between 0.60 and 1.50 are processed, ensuring we only count roughly spherical drops.
  Area Limits: Filtered out tiny artifacts and massive light flashes by restricting valid contour areas to 15 < A < 1000 pixels.
Relevant Calculations (Shape & Filter Math)
Filtering Noise vs. Actual Droplets

## Slide 6
4
  Centroid Mapping: The geometric center of every valid droplet is calculated as:
C = (x + w/2, y + h/2)
  Frame-to-Frame Distance: We use the SciPy library to compute the Euclidean distance matrix between existing tracked centroids (x1, y1) and new centroids (x2, y2) in the current frame:
D = sqrt{(x2 - x1)^2 + (y2 - y1)^2}
  Tracker Logic: If D is less than our threshold of 150 pixels, the algorithm successfully links the new position to the existing droplet ID, preventing duplicate counts.
  The brain of the system is the Centroid Tracker. It calculates the exact center of every drop and maps their Euclidean distance between frames. This mathematical proof allows the system to assign a unique ID to every single drop and track its exact path down the column without double-counting.
Relevant Calculations
The Centroid Euclidean Distance Matrix

## Slide 7
5
  The Initial Approach: We attempted to use physical optical sensors, including infrared break-beams and point-laser diodes, to cross the 10+ cm glass column.
  The Refraction Problem: Because the continuous phase acts as a cylindrical lens, and the dispersed droplets act as moving spherical lenses, the laser light refracted unpredictably.
  The Wobble Effect: Fluid dynamics dictated that the 2–4 mm drops fell in non-linear, wobbling paths, frequently missing the narrow physical sensor beams.
  The Solution: We abandoned the physical optical grid and engineered a dynamic, camera-based Computer Vision (CV) framework to monitor the entire column simultaneously.
  Also we tried using dye to the dispersed phase is a common quick fix for improving contrast in fluid dynamics but it had its own drawbacks dyes can act as weak buffers or competing indicators. They might shift the actual pH at which the phenolphthalein triggers or worse react with the acetic acid/base in your titration. So by this we could end up with a "False Endpoint" or a sluggish color transition that doesn't represent the true chemical equivalence point.
Difficulties Faced & The Pivot
Why Hardware Sensors Failed

## Slide 8
5
  We faced severe challenges trying to make hardware lasers work. The curved glass column and the refractive index of the continuous phase scattered our laser beams, and the droplets wobbled out of the sensor path. To tackle this, we shifted our entire approach to software, building a computer vision model that monitors the whole column at once.
Difficulties Faced & The Pivot

## Slide 9
  The Virtual Tripwire: Established a single Y-coordinate axis (e.g., Y=184).
  Detection Logic: A drop is only counted when its centroid history proves it moved downward across the line: Y_prev < Y_tripwire < Y_current.
  Data Logging: Achieved highly accurate counting. The system automatically pushes the Bubble ID, Timestamp, Frame Number, and (X,Y) coordinates into a bubble_log.csv for post-experiment analysis.
Results & Tripwire Execution
Perfect Counting Accuracy

## Slide 10
7
  Cost-to-Performance: Successfully replicated the functionality of expensive analytical hardware (like Phase Doppler Analyzers) using an off-the-shelf camera and Python processing.
  Resilience: The live trackbar HUD proved that the system could be tuned on-the-fly to adapt to changing laboratory lighting conditions.
  This Innovation Lab project proves that software-driven analytical instruments can outperform rigid hardware setups in complex fluid dynamics. We successfully built a highly resilient, low-cost sensor that can easily be scaled to calculate terminal velocity and other hydrodynamic properties in industrial setups."
Conclusion & Innovation Lab Takeaways
Industry 4.0 Applicability

## Slide 11
Thank You